## Slide 1: Fallopian Tube Isolator Progress
Alexander Padovano
Alexander Xu
Thomas Prose
Group 18

## Slide 2: Sterilization Methods
Laparoscopic Procedure: Hysteroscopic Essure Sterilization
  4306 women between 2003 & 2010
Tubal Ligation
  635,000 procedures annually (8-9% of live births)
  325,000 are post-partum minilaparotomy bilateral tubal ligation
  Most common method of contraception in women over 35
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 3: Tubal Sterilization Alternatives
Implanon
  Placed in skin above upper arm
  Up to 3 years of contraception
  Affects levels of progestin
  Similar to oral contraception
Levonorgestrel Intrauterine Device
  Provides effective birth control for 5 years
  Relies on local effects of progesterone
Copper Intrauterine Device
  Provides effective birth control for 10 years
  Inserted and removed through the cervix
  Hormone Free
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 4: Post-partum Minilaparotomy Bilateral Tubal Ligation
Permanent sterilization option
Within 48 hours of normal birth
325,000 procedures annually
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 5: Post-partum Minilaparotomy Bilateral Tubal Ligation
3 Common Methods of Occlusion
  Modified Pomeroy
  Filshie Clip
  Parkland
Same Technique for Isolation and Visualization
  Ideal situation, use fingers
  Generally, use army navy retractor to “fish” for fallopian tubes
  Babcock clamp secures the tube
Design Needs to Follow Same Procedure
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 11: What’s the Problem?
Morbidly Obese Patients
Target farther away
Organs compressed
More invasive procedure required
Increased surgery duration
2-3 cm
10-15 cm
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 12: Project Scope
Task
Design instrument to act as retractor
Purpose
To isolate and secure the fallopian tubes during post-partum minilaparotomy bilateral tubal ligation
Intent
Streamline the procedure
Client: Dr. Vincent Padovano, M.D. OB/GYN
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 13: Design Specifications
12” long
1” wide
Thick enough to remain relatively undeformed under procedural conditions
Relatively Inexpensive (to manufacture and sell)
  Army Navy Retractors cost ~$15.00 - $20.00
Groove to isolate fallopian tube
Locking mechanism to secure the fallopian tube
Rounded edges and shallow curves to avoid internal damage
Ambidextrous
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 14: Design Options
Existing solutions
  Army navy retractor
  CooperSurgical Tubal Retractor
    Discontinued
New Design Considerations:
  Head to isolate fallopian tube
  Locking mechanism to secure tube
  Materials
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 15: Head Design
Currently no specialized head design for isolating fallopian tube
Three possibilities for notch shape:
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS
Notch 1
Notch 2
Notch 3

## Slide 16: Head Design (Pugh Chart)
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS
Notch 1
Notch 2
Notch 3
Head Design | Weight | Notch 1 | Notch 2 | Notch 3 | Army/Navy
Simplicity | 4 | 4 | 4 | 4 | 10
Hook Effectiveness | 8 | 2 | 6 | 8 | 0
Safety | 10 | 10 | 8 | 6 | 8
Client’s Opinion | 8 | 6 | 8 | 2 | 4
Total | n/a | 172 | 208 | 156 | 152

## Slide 17: Locking Mechanism (Trigger) Design
Currently no existing solutions for such a device
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 18
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS
Locking Mechanism (Trigger) Design Spring Locking Mechanism

## Slide 19
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS
Locking Mechanism (Trigger) Design Passive Sliding Mechanism

## Slide 20: Locking Mechanism (Pugh Chart)
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS
Locking Mechanism | Weight | Spring-Loaded | Passive Slider
Cost | 5 | 4 | 6
Simplicity | 7 | 4 | 6
Ergonomics | 10 | 8 | 4
Ease of Use | 10 | 8 | 4
Safety | 5 | 8 | 9
Total | n/a | 258 | 197

## Slide 21: Materials Analysis
Typical post-partum uterus 1 kg at most
Device at held at ~6” from end, and 1” wide
Allow less than 1% (of length) deflection with 10 * maximum expected weight (10*1 kg = 10 kg)
1% * 6” = 0.06” = 0.0015 m
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 22: Materials Analysis (Continued)
Model shaft as rectangular prism
Deflection: y = WL^3/(3EI), E is Young’s Modulus, I is moment of inertia, W = 10 kg, L = 6” = 0.15 m
Moment of Inertia I = hb^3/12, b & h are cross-sectional dimensions, b = 1” = 0.0254 m
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 23: Materials Analysis (Continued)
“Surgical” Stainless Steel: E = 180 GPa
  As low as $1000/metric ton
  Thickness needed for 1% deflection:
    y = WL^3/(3EI), I = b^3*h/12
    h = (4wL^3)/(Eyb^3) = 3*10^-5 m
Aluminum: E = 69 GPa
  As low as $2000/metric ton
  Thickness needed for 1% deflection:
    h = (4wL^3)/(Eyb^3) = 8*10^-5 m
ABS Plastics: E = 2.3 GPa
  As low as $100/metric ton
  Thickness needed for 1% deflection:
    h = (4wL^3)/(Eyb^3) = 2.4*10^-3 m
Ultra High Density Polyethylene: E = 0.69 GPa
  As low as $1000/metric ton
  Thickness needed for 1% deflection:
    h = (4wL^3)/(Eyb^3) = 8*10^-3 m
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 24: Materials (Pugh Chart)
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS
Material | Weight | SS (316) | Al | ABS Plastics | HD Poly.
Cost | 2 | 7 | 5 | 10 | 8
Strength | 8 | 10 | 8 | 4 | 2
Sterilization | 6 | 10 | 10 | 4 | 4
Manufacturing | 4 | 8 | 8 | 6 | 6
Total | n/a | 186 | 166 | 100 | 80

## Slide 25: Final Design
Groove deepest in the middle to balance “hook” effectiveness and safety (avoiding internal damage)
Spring-loaded trigger/locking mechanism for easy release and reload
Stainless steel composition for balanced strength, cost, ease of sterilization, as well as simplicity in manufacturing
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 26: Final Design Summary
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS
Note: Drawing does not include trigger/locking mechanism in drawing

## Slide 31: Task Organization
TOM PROSE | ALEX PADOVANO | ALEX XU
BACKGROUND RESEARCH | VISUAL DESIGNER, CLIENT CONTACT | CALCULATIONS, WEBMASTER
PRESENTATION 1 | PRESENTATION 3 | PRESENTATION 2
FIRST PAPER LEAD WRITER | THIRD PAPER LEAD WRITER | SECOND PAPER LEAD WRITER
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 32: Planned Tasks
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS
3D-printed prototypes from CAD models
Ergonomics Testing with Physical Protoypes
Client Feedback
Finalize Design

## Slide 33: Updated Timeline
 | SEPTEMBER |  |  |  | OCTOBER |  |  |  | NOVEMBER |  |  |  |  |  |  |  | DECEMBER | 
CHOOSE TOPIC |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PATENT/LIT SEARCH |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FINALIZE LOCKING MECHANISM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SELECTED DESIGN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MATERIALS SEARCH COMPLETE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1st PHYSICAL PROTOYPE (w/ CAD MODELS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SIMULATED TESTING (ERGONOMICS) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLIENT FEEDBACK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2nd PHYSICAL PROTOYPE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ERGONOMICS TESTING |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLIENT FEEDBACK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FINAL DESIGN/PHYSICAL MODEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BACKGROUND PROBLEM PROJECT SCOPE DESIGN ANALYSIS TASKS

## Slide 34: References
Post-partum Tubal Sterilization:http://emedicine.medscape.com/article/1848524-overview#a15
Complications of Essure Sterilization:http://www.ncbi.nlm.nih.gov/pubmed/22360159
Tubal Sterilization Treatment and Management: http://emedicine.medscape.com/article/266799-treatment#a1132
Implanon Contraceptive Implant: http://www.mayoclinic.com/health/implanon/MY01007
Intrauterine Devices: http://www.webmd.com/sex/birth-control/intrauterine-device-iud-for-birth-control
Metal prices: http://www.lme.com/home.asp
Materials “Market:” http://www.alibaba.com/showroom/
Plastics: http://www.plastic-products.com/spec11.htm
Young’s moduli: http://www.engineeringtoolbox.com/young-modulus-d_417.html

## Slide 35: QUESTIONS?